## Slide 1: Source Water Protection and Development - Conflicts and Convergence
2015 New England Water Works Association Symposium
Devens, Massachusetts
October 22, 2015

## Slide 2: Truslow Resource Consulting LLC
:: 454 Court Street :: Suite 304 :: Portsmouth, NH 03801 :: (603) 766-6670 :: www.truslowrc.com
Danna Truslow, PG, CG – Principal Hydrologist
Samantha Wright – Geomorphologist and GIS Specialist
Anna Boudreau – Land Conservation Consultant, Training and Outreach

## Slide 3: ..or The Evolving Role of Local Planning and Land Conservation in Protecting Aquifers for Future Community Water Supplies
Notes: Protect the resource
Without preventing future community water supply

## Slide 4: Significant but Limited Sand and Gravel Deposits
From USGS HA-730-M
Notes: Stratified drift and ice contact
Focus on small area in red box – SE New Hampshire

## Slide 5: Focus Area Brentwood and Kingston, NH

## Slide 6: Conflicts
Past/existing land use in high value aquifer areas
Local control of water resources - commercialization
New board /commission members
Land use restrictions in future water supply areas
Encourage commercial development
Increased infiltration in aquifer/water resource areas – water quality impacts – road salt, landscaping chemicals, other emerging contaminants?

## Slide 7: NH – 1982 Early Aquifer Protection Planning Document Overlay districts – 1990’s
Notes: Completed through an internship with SENH Planning Commission and NH Water Resource Research Center – 5 USGS publications that defined the sand and gravel resource
All you need to know about groundwater and how to protect it

## Slide 8: Brentwood, NH
Aquifer Protection Overlay District – 1992
Active Land Protection Efforts – Conservation Commission and Regional Land Trust
Agricultural – semirural transition
Private Bottling Company – reaction
Balancing growth and protection
2015 NR Ordinance update and LP/WSR Inventory

## Slide 9: NHDES Registered Wells in Brentwood
Wells registered since 1984 |  | 
Well Water Source | Number of Wells | % of total wells
Sand and Gravel | 34 | 8%
Bedrock | 385 | 92%
Total | 419 | 
Summary of public water supply characteristics |  |  |  |  | 
Groundwater Source | # of active systems | # Active in Aquifer Zone | # of active community wells | # of active Transient, non-community | # of active Non-Transient, non-community
Sand and Gravel | 3 | 2 | 2 | 1 | 0
Bedrock | 15 | 8 | 2 | 5 | 8
Total | 18 | 10 | 4 | 6 | 8

## Slide 10: Co-Occurrence of Resources
Notes: Reduce area around town, label ponds, major rivers

## Slide 11
Notes: Point out Pine Road and Route 125
Sand and gravel extraction
Industrial/commercial activity

## Slide 13
Conserved Lands in Brentwood
By the Numbers:
~3,279 acres of conserved land
~30% of Brentwood land is conserved

## Slide 14
Conserved Lands within Aquifer
~ 756 acres of aquifer are conserved land
~20% of aquifer is conserved

## Slide 15
Water Supply Development Restrictions on Conserved Land
~ 530 acres of conserved land in aquifer has water supply use restrictions
~70% of currently conserved land has water supply use restrictions
~14% of aquifer has water restrictions written into a conservation easement

## Slide 16
Close-up – Groundwater, Surface Water and Wetland Resources in NE Brentwood

## Slide 17
Close-up – Groundwater, Surface Water and Wetland Resources in SE Brentwood
Note: Wetlands are not shown for Exeter

## Slide 18: Ordinance Update
Water Resource 101
Better definition of resource
Co-occurrence of resources
Impact of new local stormwater regulations on resource
Improve consistency and ease of use
Provide outside resources/references
Prioritize land conservation and water supply restrictions in aquifer district

## Slide 20: Kingston, NH
Aquifer Protection Overlay District – 1990
Active Land Protection Efforts – Conservation Commission and Regional Land Trust
Agricultural – semirural transition
Groundwater monitoring at permitted developments?
2011 Aquifer Protection Ordinance update
Industrial/commercial along Rt 125 – allow additional growth?

## Slide 21: Registered Wells in Kingston

## Slide 22
Baseline data to understand existing water quality
1079 wells registered since 1984
23% in stratified drift aquifer
31 Active Public water supplies
152 Potential Contaminant Sources in Kingston – 70% in aquifer
Notes: Circles with number are registered public water supply wells
Red dots are PCS’s, multiple sources on several sites
Large circles are community water supply wells

## Slide 23
Zone A
Zone A
Zone B
Zone B
Proposed Aquifer Protection District
Boundaries A and B
Protects Most Vulnerable Resource Area
Provides Land Use Flexibility

## Slide 24
Conservation Lands
What are Water Supply Restrictions?

## Slide 25: Kingston – to do
Revisit overlay district – new development?
Future Water District?
Evaluate water supply land use restrictions
Refocus land protection efforts?
Groundwater monitoring at permitted developments – what real water quality impacts?

## Slide 26: Regional Efforts Southeast Watershed Alliance Piscataqua Region Estuaries Partnership Ordinance Review and Priorities
PREPA 2015
NOT in SCOPE

## Slide 27
Convergence - Municipal Awareness and Action
Historic use of lands
Current resource and threats
Current and future /land/water resource needs and goals – Master Plan
Board/Commission engagement, training and coordination
Economics – Attention now can save municipality in long run
Track – control emerging impacts through BMPs
Revisit and Refocus Regularly
Notes: Protect the resource
Without preventing future community water supply

## Slide 28: Questions?